	3-phase to 2-phase voltage converter
in palette

in diagram
The unit implements the conversion of three-phase voltage to two-phase voltage. Voltage values at the output are calculated as follows: / left lbrace stack{ U_d(t) ~=~ {{2} over {3}} cdot U_a(t) ~-~ {{1 over 2} cdot (U_b(t)+U_c(t))}, # U_q(t) ~=~ {{1} over {sqrt{3}}} cdot (U_b(t)-U_c(t)), } right none (1) / where U_d(t), U_q(t) are phase voltages of 2-phase current (output signals); / U_a(t), U_b(t), U_c(t) are phase voltages of 3-phase current (input signals). / The unit has 3 input and 2 output ports. / Input signals: / 1) Voltage U_a(t) , V. / 2) Voltage U_b(t) , V. / 3) Voltage U_c(t) , V. / Output signals: / 1) Voltage U_d(t) , V. / 2) Voltage U_q(t) , V. / Note: in place of phase voltages a phase currents can be applied to inputs to convert three-phase current to two-phase one.