	Symmetrical pulse-width modulator
in palette

in diagram
The unit implements the model of symmetrical pulse-width modulator (PWM). / Input analog signal U(t) is normalized on U_max : / tilde {U}(t) = {U(t)} over {U_max} / and compared with symmetrical sawtooth signal appearing as: / P(t) = left lbrace stack{ -A(t)+1, ~ if ~ A(t) < 2# +A(t)-3, ~ if ~ A(t) >= 2, } right none / where A(t) = 4 cdot frac ( t over T_0) / Record frac ( t over T_0) means a fractional residue of division: frac ( 3.43 over 3) = 0.43 . / Output signal is equal to: / y(t) = left lbrace stack{ +U_max, ~ if ~ tilde U(t) > P(t),# 0, ~ if ~ tilde U(t) = P(t),# -U_max, ~ if ~ tilde U(t) < P(t), } right none / The unit has 1 input and 1 output ports. / Input signal: / 1) Voltage U(t) , V. / Output signal: / 1) Modulated signal y(t) . / Properties: / Sampling period T_0 , s. / Maximum value of the signal, with which the saturation state occurs U_max .