	Non-symmetrical pulse-width modulator
in palette

in diagram
The unit implements the model of non-symmetrical pulse-width modulator (PWM). / Input analog signal U(t) is normalized on U_max : / tilde {U}(t) = {U(t)} over {U_max} / and compared with symmetrical sawtooth signal appearing as: / P(t)=frac ( t over T_0) . / Record frac ( t over T_0) means a fractional residue of division: frac ( 3.43 over 3) = 0.43 . / Output signal is equal to: / y(t) = left lbrace stack{ sign[U(t)] cdot U_max, ~ if ~ abs{tilde U(t)} >= P(t),# 0, ~ if ~ abs{tilde U(t)} < P(t), } right none / The unit has 1 input and 1 output ports. / Input signal: / 1) Voltage U(t) , V. / Output signal: / 1) Modulated signal y(t) . / Properties: / Sampling period T_0 , s. / Maximum value of the signal, with which the saturation state occurs U_max .