	Reducer
in palette

in diagram
The unit implements a mathematical representation of mechanical transmission (one-stage reducer) elementary link, in which the response rate of intermediate stages and phenomenon of friction in an elastic element on the link output shaft. / Figure 1 shows the kinematic diagram of an elementary mechanical link with the following indications: B_1 ~"and"~ B_2 are for, correspondingly, input and output shafts, q_1 ~"and"~ q_2 are for rotation angles of input and output shafts, i is for engagement instantaneous element (with gear transmission ratio i={%omega_1(t)} over {%omega_1(t)} = {dot q_1(t)} over {dot q_2(t)} > 1 ), c is for coefficient of rigidity of instantaneous elastic element, TP stands for an element characterizing the presence of internal viscous friction forces in the elastic element, Л is for instantaneous element featuring a play in engagement, J_2 is for moment of inertia at the link output shaft, which can include the moment of inertia of gear, moment of inertia of coupling and moment of inertia of the object. / Figure 1 / Dynamic equations for the unit: / left lbrace stack { {d %theta(t)} over {dt} ~=~ {%omega_1(t)} over i ~-~ %omega_2(t), ~ left ( или~ %theta(t) ~=~ {q_1(t)} over i ~-~ q_2(t) right ) ,# M_y(t) = {df_3(%theta)} over {dt} cdot left [ {F_1} cdot {{d %theta(t)} over {dt}} + G_1 cdot sign left ( {{d %theta(t)} over {dt}} right ) right ] , # {M_1(t)} ~=~ {f_3(%theta) cdot c ~+~ M_y(t)} over i, # {d %omega_2(t)} over {dt} ~=~ {f_3(%theta) cdot c ~+~ M_y(t) ~+~ M_{%SIGMA 2}(t) ~+~ M_{c 2}(t)} over J_2 , # M_{c 2}(t) = - left [ {F_2} cdot {%omega_2(t)} + G_1 cdot sign left ( %omega_2(t) right ) right ] , } right none (1) / where: / %theta(t) is for elastic element twist angle; / f_3 left ( %theta(t) right ) = left lbrace stack { %theta(t)+a, ~if~ %theta(t) ~<~ -a, # 0, ~if~ -a ~<=~ %theta(t) ~<=~ a, # %theta(t)-a, ~if~ %theta(t) ~>~ a, } right none / dot f_3 left ( %theta(t) right ) = {d f_3 left ( %theta(t) right )} over {dt} = left lbrace stack { 0, ~if~ abs {%theta(t)} ~<=~ a, # 1, ~if~ abs {%theta(t)} ~>~ a, } right none / sign left ( x(t) right ) = left lbrace stack { +1, ~if~ x(t) ~>~ 0, # 0, ~if~ x(t) ~=~ 0, # -1, ~if~ x(t) ~<~ 0, } right none – sign x(t); / i is for reduction ratio; / J_2 is for moment of inertia at the link output shaft, kg·m2; / a is for a half of link play value, rad; / c is for coefficient of rigidity of instantaneous elastic element; / F_1 is for coefficient of viscous friction in elastic element, N·m/(rad/s); / G_1 is for a moment due to internal dry friction forces available in elastic element, N·m; / F_2 is for coefficient of viscous friction on output shaft, N·m/(rad/s); / G_2 is for moment of dry friction on output shaft, N·m; / q_1(t) ,~ q_2(t) is for rotation angles of input and output shafts, rad; / %omega_1(t) ,~ %omega_2(t) is for angular speeds of input and output shafts, rad/s; / M_y(t) is for moment of internal viscous and dry friction forces in elastic element, N·m; / M_1(t) is for moment applied to input shaft; / M_{%SIGMA 2}(t) is for moment applied to output shaft; / M_{c 2}(t) is for moment of friction forces acting on output shaft. / The unit has 2 input and 2 output signals. / Input signals: / 1) %omega_1(t) – angular speed of input shaft, rad/s; / 2) M_{%SIGMA 2}(t) – moment applied to output shaft; / Output signals: / 1) %omega_2(t) – angular speed of output shaft, rad/s; / 2) -M_1(t) – moment applied to input shaft; (taken with an opposite sign!); / Properties: / Reduction ratio i; / Moment of load inertia J_2 , kg·m2; / Half of play value a, rad; / Coefficient of rigidity с, N·m/rad; / Coefficient of viscous friction in elastic element F_1 , N·m/(rad/s); / Moment of dry friction in elasticity G_1 , N·m; / Coefficient of viscous friction on output shaft F_2 , N·m/(rad/s); / Moment of dry friction on output shaft G_2 , N·m; / Initial angular speed of output shaft %omega_1(0) , rad/s; / Initial twist angle %theta(0) , rad;