	SimInTech submodel
In palette

In diagram
The unit generates "a shell" for nested diagram(-s) to be produced from both typical units and Submodels of a deeper nesting level. / Number of inputs and outputs of the unit is defined automatically in the process of filing the inner structure of the unit with units "Input Port" and "Output Port". / The dialog window is opened as follows: / · shift the mouse cursor to “Submodel” and single-click the mouse right button on that: contextual menu of the unit will be opened; / · shift the mouse cursor to option “Properties” and single-click the mouse right button on that: dialog window of the unit will be opened. / The unit (as well as many other units) has the following properties: / · Graphic representation – is intended to change the typical pictogram of the unit for any original pictogram. / · Item name – the name of the unit in the diagram window. Name of a submodel influences on global names of units positioned inside the submodel: global names of units nested in the submodel will have the following appearance: <Submodel Name>.<Unit Name> ("dot”-separated). A deeper nesting level has a similar appearance. / · Element type – the name of element type. It is used, for example, during development of own typical models, own units on the basis of SimInTech submodel. / · Prompt message – a text displayed as a prompt message, on positioning the mouse cursor on the unit in the diagram window. / · Performance visibility – flag for unit displaying during calculation (simulation). / · Color – color of the unit in the diagram window. If pictorgram is available it is the background color. / · Point data – the property commonly used as reference or for precise positioning the unit in the diagram. / · Rotation angle – rotation angle for the unit pictogram in the diagram window. / · Width – width of the unit pictogram in the diagram. / · Height – height of the unit pictogram in the diagram. / · Display the frame – flag for displaying the unit image frame in the diagram. / · Frame color – color of the unit frame in the diagram window. / · Unit signature – text (line) to be entered as a signature next to the unit in the diagram. It can be positioned randomly but relative to the unit and remains bound to that when the unit is shifted. Style (font, color, leveling) of the signature are set by other (neighbor) properties. / · Signature style – indicates what is to be displayed as the signature of the unit. / · Name of submodel file – allows the submodel pattern to be stored and edited in a separate file. / Internal diagram window of Submodel “is opened” as follows: / · by double-clicking the mouse left button in the unit field; a double-click of the mouse in the blank space of the submodel opened diagram window returns to a previous (upper) level of the diagram. / · From the drop-down context menu item “Actions” – “Enter the submodel”. / The Submodel internal structure is closed by two methods: / · by double-clicking the mouse left button in a blank space of the submodel diagram window; / · by pressing the “Arrow up” button in the tool bar of the diagram window. / Notes: / More detailed information on the operational procedures for this unit can be found in Sections “Demo tutorial” or “ Brief User’s Manual”. / Possible nesting level for submodels is not limited.