	SimInTech Input Port
In palette

In diagram
The unit is used inside the Submodel and determines the availability of an input port to that. It serves for connecting external part of the diagram to the diagram inside the Submodel. / The unit is vectorized and arranges: / reception of data from typical units and Submodels, which are external in relation to the given one; / transmission of data for their transformation by typical units (or Submodels) belonging to the inner structure of the given submodel. / A number of SimInTech Input Port units automatically determine a number of inputs to the given Submodel. / When closing the internal Diagram window, “re-drawing” of the image of the given Submodel is automatically executed. / SimInTech Input Port can process both scalar and vector input signals. / Note: it is recommended immediately after unit transfer from Typical units “Line" to the Diagram window to assign a “unique” name to such unit. E.g., Input No. 1. Double-click the unit to indicate the connection port name.