	To the Memory
In palette

In diagram
The unit is intended to link one part of the diagram to another one located in a random place of the project. Double-click the unit to indicate the point name. A number of link points in the unit can be indicated. / The unit is vectorized and performs the procedure of generation of global (named) variables in the dynamic memory to be used for implementation of the 1st stage of “wireless” data transfer (e.g., from the Main diagram window to a submodel or from a submodel to the Main diagram window or to another submodel). / The unit has only input ports (one or more). / The unit is provided with a special dialog window containing a dialog line Variable Name (to enter global variable name) and information window Variables List (to enter a list of names of all variables available in the project by the moment of dialog window opening). / By default Y1 is entered of in the 1st unit To the Memory transformed to the Diagram window in the line Variable Name. If this variable name is good for you then press Yes to generate a cognominal global variable in the dynamic memory (scalar or vector one depending on the dimension of a unit input signal). / If the default name (Y1) is saved in the 1st unit To the Memory transferred to the Diagram Window then, when opening the dialog window of the 2nd unit To the Memory transferred to the Diagram Window, name Y2 will be suggested by default, and the information window Variables List will contain 2 (two) names: Y1 and Y2. / Example of dialog window filling: / If you want to assign a unique name (e.g., dN(t)/No) to a (scalar or vector) variable then a default name shall be deleted in the dialog line and a desired name shall be entered. / Properties: Any properties shall not be set for the operation of the unit. / Notes: / To generate a vector global variable a vector input signal shall be preliminarily generated, e.g., by means of a typical Multiplexor unit. / If a number of variables is considerably big and their full list cannot be housed in one of mini windows then for displaying the whole content a standard scrolling mechanism is provided for such window.