	Multiplication by number
In palette

In diagram
The unit is vectorized and implements multiplication between each vector value element at the first input by scalar value at the second input: / y_i(t) = u_{1,i}(t) cdot u_2(t) , / where u_{1,i}(t) is for the i-th of an input vector signal at the first input; u_{2}(t) is for a signal at the second input, scalar; y_i(t) is for an output vector signal element vec{y}(t) . / Output dimension is the same as the first input dimension. / Properties: / Any properties shall not be set for the operation of the unit.