	Linear transducer
In palette

In diagram
The unit is vectorized and implements linear interpolation of input value. / At the same time the input value equal to the minimum input value corresponds to zero at the output, while the input value equal to the maximum input value corresponds to one at the output: / vec{y}(t) = {vec{u}(t) - x_min} over {x_max - x_min} or y_i(t) = {u_i(t) - x_min} over {x_max - x_min} , / where vec{u}(t) is for input vector signal, x_{min}, x_{max} are for unit properties, vec{y}(t) is for output vector signal. / Properties: / Minimum input value — x_{min} — input signal value corresponding to 0 at the output. / Maximum input value — x_{max} — input signal value corresponding to 1 at the output.