	Submodel with relay-minus with variable dead band and return band
In palette

In diagram
The unit is vectorized and appears as a submodel (assembly). To see the algorithm structure press “Actions” → “Enter to Submodel” with the right button. / The unit appears as a submodel with the relay operating algorithm with variable hysteresis (variable return band) and variable dead band. Hysteresis and dead band are set by unit input signals. Unit output signal is non-negative and the relay actuates only when a negative input signal is available (otherwise there is zero at the output). / Input signals: / Signal – a signal being processed by the unit. / Dead band – width of dead band. / Return band – width of return band. / Output signals: / Relay output – a signal equal to +1 or 0 in accordance with the unit operating algorithm. / Properties: / Any properties are not required for the operation of the unit. / Note: to implement vector processing signals subject to transformation should be “compressed” into a vector input signal by means of a typical “Multiplexor” unit.