	Bidirectional bus (output)
In palette

In diagram
The unit is vectorized and is intended to create a bidirectional communication line. / The unit has named input and output signals (by default one input signal is named as A and one input signal is named as B), and bidirectional port of data bus type (multi-core line) named as MAIN. / The unit is applied together with the Bidirectional bus (input) unit. When two such units are interconnected via the bidirectional port MAIN, mutual transmission of input signal is carried out from one unit to the output signal of the other: / The user by himself can edit the number and type of signals transmitted and received via bidirectional data bus.