	Algorithm output (vector)
In palette

In diagram
The unit is vectorized and records values of signals (data recording) in a local list of project signals or in a list of connected data base signals. The unit has one input contrary to the unit “Algorithm output” wherein a number of input ports is the same as a number of recordable signals. Dimension of output vector is equal to the sum of dimensions of recordable signals. / On double-clicking the unit, the editor for the list of recordable variables appears. / Variable name is set in the field “Signal Name”. A devoted signal corresponds to each input of the unit. / Purpose of the table fields: / No. — serial number of the signal (and of the unit, correspondingly) is assigned. / ID – identifier of the signal (input). / Receiver – description of signal “destination” (whereto the signal passes). / Marking – signal (or signal receiver) marking. / Command – command designation or name. It is used when creating algorithms for generation of command to control units for gates, motors, etc. / Signal name – name of a variable to be recorded in the data base. / In the lower portion the algorithm name is assigned, under which output signals of this algorithm will be recorded in the data base. / To the right there are options, which can be used for setting the unit appearance in the diagram, its heading display and layout of unit ports. / Properties: / Maximum value selection (OR). / Algorithm name – the name (line), names of all signals related to the algorithm are started with in the data base. / Translation to the executive system.