	OPC Client
In palette

In diagram
The unit performs reading and writing of signals to other programs using the data exchange interface according to the OPC protocol. The dimension of the input is equal to the sum of dimensions of signals specified in the corresponding parameter of the unit. The dimension of the output is equal to the sum of the dimensions of signals specified in the corresponding parameter of the unit. / Properties: / Data exchange step, in seconds. / OPC-Server Name – the name of the COM-server with which data exchange is performed. / Delay at startup, msec – the delay in milliseconds when connecting to the COM-server. / Names of readable parameters – the list of signal names in the OPC-server that the unit reads (separator; or carriage return). / Names of writable parameters – the list of signal names in the OPC-server that the unit writes (separator ; or carriage return). / Dimensions of readable parameters. / Dimensions of writable parameters.