	RS trigger with set priority
In palette

In diagram
The unit implements the RS trigger with set priority, i.e. if the level of the logical one is at the R and S inputs, then the output will take the logical one value: / y(t) = left lbrace stack{ alignl y(t- %DELTA t), ~ if u_S(t) = 0, ~"and" ~u_R(t) = 0; # alignl 1, ~ if u_S(t) = 1; # alignl 0, ~ if u_S(t) = 0, ~и ~u_R(t) = 1; } right none , / where y(t) is for the unit output signal, y(t- %DELTA t) is for the value of the output signal at previous time step of integration, u_S(t), u_R(t) are for the first and second input signals of the unit (from the English words Set (S) and Reset (R), respectively). / Properties: / Initial conditions – the initial output values. / Add an inverted output – indicates the presence of an inverted output. / Note: The trigger (trigger system) — a class of electronic devices that are able to be in one of two stable states durably, and rotate them due to external signals.