	TS trigger
в палитре

на схеме
The unit implements the TR trigger with set priority (i.e., if the logical one level is at the R and S inputs, then the output will take the logical one value) and complementing input. / If the logical one is at any of the R or S inputs, then the trigger will work as usual RS trigger (with set priority). / If the logical zero is applied to the both R and S inputs, then the trigger will take into account a signal at the T input and change its state every time when a signal at the T input is changed from logical 0 to 1 (for the "by leading edge" type of complementing input): / y(t) ~=~ neg {y(t- %DELTA t)}, ~if~ left lbrace stack{ alignl u_R(t)=u_s(t)=0; # alignl u_T(t) = 1; # alignl u_T(t- %DELTA t) =0; } right none , / or when the input signal at the T input is changed from logical one to logical zero (for the "by trailing edge" type of complementing input): / y(t) ~=~ neg {y(t- %DELTA t)}, ~if~ left lbrace stack{ alignl u_R(t)=u_s(t)=0; # alignl u_T(t) = 0; # alignl u_T(t- %DELTA t) =1; } right none / Properties: / Initial conditions – the initial output values. / Add an inverted output – indicates the presence of an inverted output. / Type of complementing input (by leading edge, by trailing edge) – the condition of actuation of the complementing input.