	Pulse by leading edge or trailing edge
In palette

In diagram
The unit forms the pulse of value 1 with duration of one step of integration, at each change of the input value from zero to one or from one to zero: / y(t) = left lbrace stack{ alignl 1, ~ if u(t) = neg u(t- %DELTA t); # alignl 0, ~ for all other cases; } right none , / where y(t) is for the unit output signal , u(t), ~ u(t- %DELTA t) are for the input signal at current time and at previous time step of integration . / Properties: any properties are not required for operation of the unit. / Note: if any real (rather then logical) signal is applied to the unit input, then the unit will be considered as one in case of u(t) > 0.5 and zero in the case of u(t) < 0.5 :