	One-Shot Generator
In palette

In diagram
The unit generates a pulse of the y_true size with the specified duration T when an input value changes to the preset threshold u_o . / Suppose that at the point of time t_o an input value has reached the preset threshold value: u(t_0) >= u_o, ~"and"~ u(t_0- %DELTA t) < u_0 . Then in the following time: / y(t) = left lbrace stack{ alignl y_true, ~ "at" ~ t_0 <= t < t_0 + T; # alignl y_false, ~ "at" ~ t >= t_0+T ~ ("till next reaching to the threshold"); } right none / where y(t) is for the output signal of the unit, and u(t), ~ u(t- %DELTA t) are for the input signals at the current time and at the previous time step of integration. / Properties: / Pulse duration – the parameter T . / Response level — the parameter u_o . / Value of True – the pulse size y_true . / Value of False – the pulse size y_false . / Output type – the type of the unit output: typical or inverse. If the output is inverse, then on reaching the threshold value, the value y_false will be formed at the output (instead of the y_true , as for typical case).