	Two-step relay (SET)
In palette

In diagram
The unit is a submodel, which realizes setting of the logical one state for a two-set relay (SR-trigger). Signal transmission for the logical one setting is realized by the units named To memory and From memory, with one-step delay of integration. / For checking the algorithm structure one shall press “Actions” → “Enter the submodel” with the right button. / The unit is used together with the Two-step relay (RESET) unit, which sets logical zero state for the two-step relay. It is necessary to specify the same names of the relays in these two units. / Properties: / Relay name – the name whereby relay contacts are associated with the unit.