	Normally opened contact of the relay
In palette

In diagram
The unit realizes the logical AND operation for the unit input and a value applied to the corresponding control winding of the relay: / y(t) = left lbrace stack{ alignl x_relais(t), ~ "if" u(t)=1; # alignl 0, ~ "if" u(t)=0; } right none / where y(t) is for the output signal of the unit, x_relais(t) is for the value (state) of the relay and u(t) is for the input signal of the unit. / To see the algorithm structure, press the right button on the unit and select the item "Actions" → "Enter the submodel". Signal transmission from the control winding of the relay is realized by the unit named From memory. / Properties: / Relay name – the name whereby a control action is defined.