	Switch contact of the relay
In palette

In diagram
The unit realizes the operation of switching of input contacts depending on a value at the control winding of the relay: / y(t) = left lbrace stack{ alignl u_1(t), ~ if x_relais(t)=0; # alignl u_2(t), ~ if x_relais(t)=1; } right none / where y(t) is for the output signal of the unit, x_relais(t) is for the value (state) of the relay and u_1(t),~u_2(t) are for input signals of the unit. / To see the algorithm structure, press the right button on the unit and select the item "Actions" → "Enter the submodel". Switching of contacts is realized by the Key-3 unit, and transmission of a signal from the control winding of the relay is realized by the unit named From memory. / Properties: / Relay name – the name whereby a control action is defined.