	Rounding
In palette

In diagram
The unit performs rounding (accuracy limitation) of an input real number with the user defined accuracy. / The unit is vectorized, it is a submodel (assembly). For checking the algorithm structure one shall press “Actions” → “Enter the submodel” with the right button. / The unit algorithm realizes the following formula: / y_i(t) = p cdot integer({u_i(t)} over {p} + 0.5) , / where u_i(t) is for the input vector element, p is for the parameter that specifies accuracy of rounding, y_i(t) is for the output vector element. / Property: / Accuracy step – parameter p .