	Integrator on amplifiers
In palette

In diagram
The unit implements the function of numerical integration with limitation. / The unit is vectorized, it is a submodel (assembly). For checking the algorithm structure one shall press “Actions” → “Enter the submodel” with the right button. / The unit algorithm implements numerical integration of an input signal (signals). / Properties: / Number of variables – the number of integrable variables of the input vector. / Initial state – the values of initial states for integrals of input variables. / The unit signals: / Input signals: / Derivative — the unit is fed by a directly integrable value OR the logic signal -1, 0, +1. In the second case, the unit uses the "Time constant" signal that determines the rate of increase (decrease) of the integral. If the derivative is an integrable value, then the "Time constant" shall be set as 1. / Transmitting input – the signal which is directly transmitted to the unit output if the "Sign of transmitting" is equal to 1. / Sign of transmitting – the logic signal. If it is equal to 1, then the "Transmitting input" value will be transferred to the unit output. / Sign of fixing – the logic signal. If it is equal to 1, then the unit output signal value will be fixed and remain constant until the "Sign of fixing" will change its state to 0. / Shift of integral – it is used in special cases, it is equal to 0 on default. / Time constant – the reciprocal value of a derivative. It is used when the logic signal -1 ("less"), +1 ("more") or 0 is transferred as a derivative. If an integer value enters as a derivative (real derivative), the "Time constant" shall be set as 1. / Maximum value – the restriction of an integral "from overhead". The unit output signal can not be greater than this value. / Minimum value – the restriction of an integral "from below." The unit output signal can not be less than this value. / Output signal: / Integral – the value of the integral of derivative (with restrictions), or the transmitting input (if the sign of transmitting is used), or constant (if the sign of fixing is used).