	Signal filtering
в палитре

на схеме
The unit implements the function of numerical filtering using the "Discrete aperiodicity of the 1-st order” unit. / The unit is a submodel (assembly). For checking the algorithm structure one shall press “Actions” → “Enter the submodel” with the right button. / The unit algorithm implements numerical filtering of an input signal (signals). / Properties: / Damping constant — the parameter that specifies the time constant for the first order aperiodicity and determines degree of "smoothing" or filtering of the input signal. / Number of variables — the number of variables in the input vector. / The unit signals: / Input signals: / Sign of transmitting — if it is equal to 1, then an input variable x (without filtering) is transferred to the output. / Х — the filterable variable (variables). / Output signal: / Хf — the filtered variable (variables).