	DZG (dead zone generation)
In palette

In diagram
The unit implements a linear element algorithm with a gain equal to 1 and a dead zone, which is specified by the unit parameters. / The unit is a submodel. For checking the algorithm structure one shall press “Actions” → “Enter the submodel” with the right button. / Properties: / Dead zone – the absolute value of the high and low bounds of switching-over for the "Relay-controlled with a dead zone" unit. / Return zone – the value of the return zone for the high and low bounds of switching-over. / Input signals: / Input – the input signal of the unit. / Output signal: / Output – it is equal to the input signal, if it goes beyond the dead zone (with provision for the return zone). It is equal to 0, if the input signal is within the dead zone.