	External DLL
In palette

In diagram
The unit is a tool for connection of a previously compiled library to the design model. In this case a significant increase in calculation speed is achieved, as well as a possibility to calculate several typical objects on the base of the same algorithm. In addition, the unit permits to perform a calculation by several flows. / Properties: / Port capacity — the number of input signals applied to a design model (to DLL). / Array of dimensions of outputs — the array in which dimensions of outputs from DLL are indicated. / Names of loadable DLL — the names of pre-compiled DLL that are loaded into the model. One DLL is indicated or in case of several DLLs they are divided by semicolon. / Names of equipment — the names of equipment (components) that are inserted in inputs/outputs of a DLL scheme. One DLL permits to calculate a lot of objects. The names are separated by semicolons. / Names of project files for debugging — the names of project files, suitable to downloadable DLL; they are used for debugging (in the process of calculation) of schemes embedded in the DLL. / To create nonexistent variables on default — to create variables (that do not exist) in the database for calculated equipment (components). / Number of flows — the number of flows, in which the objects (components) of the DLL will be calculated.