	Vector AND
In palette

In diagram
The unit is an analogue to the "AND" logical unit, it is vectorized and operates to the following algorithm: / y(t) = left lbrace stack{ alignl 1, ~ if all ~ u_{i,j}(t) = 1; # alignl 0, ~ if at least one of ~ u_{i,j}(t) = 0; } right none , / where y(t) is for the output scalar signal of the unit, u_{i,j}(t) is for the i-th element of the j-th input vector signal. / Property: / Port capacity — the number of the unit input signals.