	Two-position relay (RS)
In palette

In diagram
The unit is a submodel containing the RS-trigger with reset priority. For checking the algorithm structure one shall press “Actions” → “Enter the submodel” with the right button. / Properties: / Relay name — the name of the variable at the RS-trigger output that is transferred to the “To Memory” list of signals. / Input signals: / S – set, the setting of the RS-trigger in the logical one state. / R – reset, the reset of the trigger to the logical zero state. / If both inputs are equal to the logical one, then the logical zero will be at the output because of reset priority.