Equation counter
	Boundary electric node
in palette	| System of linear equations |

in diagram
The unit implements the model of constant potential source described via the following equation: / U_i(t) cdot 1 = U_0 / where: / U_i(t) is for potential of a given node; / U_0 is for boundary potential value. / The unit is a submodel, in which a block diagram consisting of system of linear equations library units is implemented: / Figure 1 / The constant referred to as 1 in the diagram sets up a coefficient equal to 1 in the system of equation with number of column equal to number of line, which is generated at unit “Equation counter” output, using unit “Setting of coefficients of equation for node”. The right part of equation is generated using the constant U0. At its output this unit uses the indirect connection generating unit to generate the potential value (connection named U) and number of potential variable of this node in the vector of solutions for the system of linear equations (connection named NSELF). / Property: / Node potential, V – a number defining the potential value in the node. / Samples for filling in the dialog window for unit properties: / Numerical definition of properties: / Name Value / Node potential, V [10] / Named definition of properties: / Name Value / Node potential, V [u0] / Notes: / Unit property can be scalar only. / Named property is set up as local variable of model (or submodel) in Parameters tab or as a global signal of the project via Graphics → Signals main menu option. / Inderect group connection unit / Inderect group connection unit / Output circuit 1 / Unit “Submodel output” / Setting of coefficients of an equations for the node