Multiplication of conductivity coefficients for adjacent nodes for -1
Node potential output
Inderect group connection unit
Summing of current of sources
Equation number generation
Integration of numbers of columns
Setting of coefficients of an equation for the node
Diagonal coefficient
Inderect group connection unit
output circuit 1
output circuit 2
	Potential electric node
in palette	| System of linear equations |

in diagram
The unit implements and describes the balance equations for currents in the node along with calculation of nodal potential. The following equation is generated for each unit of this a type: / sum from {j=1} to {n} left ( u_i(t) - u_j(t) right ) cdot k_{i j} ~=~ sum from {j=1} to {n} i_{src i j} (t) / where: / u_i(t) is for potential of a considered node; / u_j(t) is for values of potentials of nodes the considered node is connected with; / k_{i j} is for coefficients of conductivity of elements connecting this (i-th) and adjacent (j-th) nodes; / i_{src i j} is for source current supplied to this node (i) from the adjacent node (j). / After transformation, this equation acquires the appearance, which is used for modeling an electronic node: / u_i(t) cdot sum from {j=1} to {n} k_{i j} ~-~ sum from {j=1} to {n} left ( u_j(t) cdot k_{i j} right ) ~=~ sum from {j=1} to {n} i_{src i j} (t) / Internal structure of this unit is given in Figure 1: / Figure 1 – Internal structure of unit “Electric circuit branching” / Using indirect connection generating units from output 1 and output 2, to which the edges of electric circuit are connected, values for numbers of equations of adjacent nodes (NJ), coefficients of conductivity to adjacent nodes (KJ) and values of current of sources between the considered and adjacent nodes (Isrc.) are obtained. Then numbers of equations of adjacent nodes are multiplexed to a vector and the number of appropriate equation, which is generated by the equation number generating unit, is added to the vector end. In the similar manner values of coefficients of conductivity are multiplexed, then coefficients of conductivity are multiplied by -1 by means of unit “Amplifier”, and the sum of all conductivities, received from adjacent nodes and obtained by means of unit "Vector elements sum-up” (unit designated as “Diagonal coefficient”), is added as a last element of the sum vector of conductivities. Right parts of equations are formed as a sum of all currents of sources relative to adjacent nodes. At its output this unit uses indirect connection generating unit to generate the potential value (connection named U) and number of potential variable of this node in the vector of solutions of the system of linear equations (connection named NSELF). / Property: / Initial node potential, V – a number defining the initial value of potential in the node. / Samples for filling in the dialog window for unit properties: / Numerical definition of properties: / Name Value / Initial node potential, V [-5] / Named definition of properties: / Name Value / Initial node potential, V [u1_0] / Notes: / Unit property can be scalar only. / Named property is set up as local variable of model (or submodel) in Parameters tab or as a global signal of the project via Graphics → Signals main menu option.