Input circuit
output circuit 1
output circuit 2
Summing of current of sources
	Electric circuit branching
in palette	| System of linear equations |

in diagram
The unit ensures the division of electric circuit boundary or internal node output for connecting more than two edges to one node. / The unit has one input and two outputs; besides, it enables sum-up of currents of sources. / Internal structure of the unit is shown in Figure 1: / Figure 1 / This unit uses units “Multiplexor” to integrate values of coefficients of conductivity and numbers of adjacent nodes into a united vector and sum up currents of sources as well. / Properties: no properties are required for operation of the unit.