	Controllable voltage source
in palette	| System of linear equations |

in diagram
The unit represents the model of a source of controllable difference of potentials, which can be described via the following equation: / {u_i(t) - u_j(t)} = U_0 , / where: / u_i(t) is for potential of the given node; / u_j(t) is for potential of previous (input) node; / U_0 is for value of boundary potential. / Internal structure of the unit is given in Figure 1: / Figure 1 – Internal structure of unit “Controllable voltage source” / The unit has an input (from the bottom), which is connected to the boundary or internal node of the electric circuit, a control input (on its side) for setting up the difference of voltage source potentials and an output for connection to other electric circuit elements. This element is topologically a node of special type. / The constant sets up coefficients equal to 1 and -1 by means of unit “Setting up of equation coefficients for node” 2 in the system of equations with numbers of columns equal to the number of line, which is generated at the output of unit “Counter of equations”, and to the number of previous node. The right part of the equation is generated from input “Control”. / At its output this unit uses indirect connection generating unit to generate the potential value (connection named U) and number of potential variable of this node in the vector of solutions of the system of linear equations (connection named NSELF). At the same time the source current is directly transmitted to previous node. / Property: / Shunt resistance, Ohm – a number setting up the shunt resistance value. / Examples for filling in the dialog window for unit properties: / Numerical definition of properties: / Name Value / Shunt resistance, Ohm [1e8] / Named definition of properties: / Name Value / Shunt resistance, Ohm [Rsh_1] / Notes: / Unit property can be scalar only. / Named property is set up as local variable of model (or submodel) in Parameters tab or as a global signal of the project via Graphics → Signals main menu option. / Calculation of the potential of output at step / coefficients / Control / Input circuit / Setting of coefficients and right part / output circuit 1