Input circuit
Input circuit 2
Conductivity
supply current
	Linear electric resistance
in palette	| System of linear equations|

in diagram
The unit represents a linear resistance model described by the Ohm's law: / {u_1(t) - u_2(t)} over R = I(t) , / where: / u_1(t) , u_2(t) is potentials of nodes this element is connected to; / R is for resistance value; / I(t) is for current through element. / Internal structure of the unit is given in Figure 1: / Figure 1 – Internal structure of unit “Linear electric resistance” / This unit by means of indirect connection generating units transmits conductivity values (KJ), which are calculated as 1/R, and values of currents (Isrc), equal to zero, to electric circuit internal nodes connected to this element. At the same time the value of own node number (NSELF) from the first input is transmitted as the value of adjacent node number (NJ) and vice versa. / Property: / Resistance, Ohm – a number setting up the resistance value R. / Examples for filling in the dialog window for unit properties: / Numerical definition of properties: / Name Value / Resistance, Ohm [5] / Named definition of properties: / Name Value / Resistance, Ohm [R1] / Notes: / Unit property can be scalar only. / Named property is set up as local variable of model (or submodel) in Parameters tab or as a global signal of the project via Graphics → Signals main menu option.