Input circuit
Input circuit 2
Inductance L
# step
	Ideal inductance
in palette	| SLAE |

in diagram
The unit represents a non-linear resistance model described by the following differential equation: / u(t) = L cdot {{di(t)} over {dt}} , / where / u(t) is for difference of potentials; / L is for inductance; / i(t) is for current. / Unit of “Integrator” type is not allowed to be directly used for current calculations since it would lead to one-step delay and non-convergence of numerical diagram implemented in this method for making electric circuit models. Thus, an implicit calculation pattern for inductance (and capacitance, as well) elements shall be applied here. / This differential equation can be reduced to an algebraic one by means of approximation of its derivate using the Euler inverse formula in the simplest case: / i^[n+1] = i^[n] + h over L cdot u^[n+1] , / where: / u^[n+1] is for difference of potentials of nodes at step n+1, to which this element is connected; / h is for step of integration; / i^[n+1] is for current through element at step n+1; / i^[n] is for current through element at step n; / In accordance with this relation the inductance can be represented as a linear resistance with conductivity equal to: / y = h over L , / with current source equal to: / i_src = i^[n-1] + h over L cdot u^[n] . / Figure 1 – Internal structure of unit «Ideal inductance» / Figure 1 shows an inductance approximation diagram correspondent to the above mentioned relations and graphically represented in the development environment for SimInTech-4 programming system. / Properties: / Inductance, H – a number defining inductance value. / Initial current, А – a number defining current initial value. / Examples for filling in the dialog window for unit properties: / Numerical definition of properties: / Name Value / Inductance, H 0.6 / Initial current, А 0.0 / Named definition of properties: / Name Value / Inductance, H L0 / Initial current, А i0 / Notes: / Unit property can be scalar only. / Named properties are set up as local variable of model (or submodel) in Parameters tab or as global signals of the project via Graphics → Signals main menu option.