Input circuit
Input circuit 2
Control
	Variable inductance
in palette	| System of linear equations |

in diagram
The unit is a non-linear resistance model described by the following differential equation: / u(t) = L(t) cdot {{di(t)} over {dt}} , / where / u(t) is for difference of potentials; / L(t) is for inductance, time-variant (inductance value is supplied to input port of unit “Control”); / i(t) is for current. / The unit is similar to unit Ideal Inductance. / Figure 1 – Internal structure of unit “Variable inductance” / Figure 1 shows a variable inductance approximation diagram graphically represented in the development environment for SimInTech-4 programming system. / Property: / Initial current, А – a number defining current initial value (for unit of delay by one-step of integration). / Examples for filling in the dialog window for unit properties: / Numerical definition of properties: / Name Value / Initial current, А 0.0 / Named definition of properties: / Name Value / Initial current, А i0 / Notes: / Unit property can be scalar only. / Named property are set up as local variable of model (or submodel) in Parameters tab or as global signal of the project via Graphics → Signals main menu option.