Input circuit
Input circuit 2
	Ideal electric capacitance
in palette	| System of linear equations |

in diagram
The unit represents a non-linear resistance model described by the following differential equation: / i(t) = C cdot {{du(t)} over {dt}} , / where / u(t) is for difference of potentials, V; / C is for capacitance, F; / i(t) is for current, А. / Unit of “Integrator” type is not allowed to be directly used for current calculations since it would lead to one-step delay and non-convergence of numerical diagram implemented in this method for making electric circuit models. Thus, an implicit calculation pattern for inductance (and capacitance, as well) elements shall be applied here. / This differential equation can be reduced to an algebraic one by means of approximation of its derivate using the Euler inverse formula in the simplest case: / i^[n+1] = C over h cdot u^[n+1] - C over h cdot u^[n] , / where: / u^[n+1] is for difference of potentials of nodes at step n+1, to which this element is connected; / u^[n] is for difference of potentials of nodes at step n, to which this element is connected; / h is for step of integration; / i^[n+1] is for current through element at step n+1; / In accordance with this relation the capacitance can be represented as a linear resistance with conductivity equal to: / y = C over h , / with current source equal to: / i_src = - {C over h} cdot u^[n] . / Figure 1 – Internal structure of unit “Ideal electric capacitance” / Figure 1 shows a capacitance approximation diagram correspondent to the above mentioned relations and graphically represented in the development environment for SimInTech-4 programming system. / Property: / Capacitance, F – a number defining the capacitance value. / Examples for filling in the dialog window for unit properties: / Numerical definition of properties: / Name Value / Capacitance, F 1e-4 / Named definition of properties: / Name Value / Capacitance, F с5 / Notes: / Unit property can be scalar only. / Named properties are set up as local variable of model (or submodel) in Parameters tab or as global signals of the project via Graphics → Signals main menu option.