Input circuit 1
Input circuit 2
supply current
Dependance of conductivity on voltage
Conductivity integration selection unit
	Non-linear electric element
in palette	| System of linear equations |

in diagram
The unit represents a non-linear resistance model described by the following relation: / left ( {u_1(t) - u_2(t)} right ) cdot y left ( {u_1(t) - u_2(t)} right ) = I(t) / where: / u_1(t) , u_2(t) are for potentials of nodes, the considered element is connected to; / y left ( { u_1(t) - u_2(t)} right ) is for conductivity-voltage drop dependance function; / I(t) is for current through element. / Internal structure of the unit is given in Figure 1: / Figure 1 – Internal structure of unit “Non-linear electric element” / This unit by means of indirect connection generating units transmits conductivity values (KJ), which are calculated as a function from the difference of input potentials, and values of currents (Isrc), equal to zero, to electric circuit internal nodes connected to this element. To ensure correct selection of conductivity the convergence is checked by comparing the conductivities at preliminary stage and at final stage. The value of own node number (NSELF) is transmitted as the value of adjacent node number (NJ) and vice versa / Properties: / Drop of voltages, V – vector defining the values of drop of voltages. / Conductivity, 1/Ohm – vector defining the conductivity of element with voltages specified for the first property. / Examples for filling in the dialog window for unit properties: / Numerical definition of properties: / Name Value / Drop of voltages, V [-2,-1,0,1,2,3] / Conductivity, 1/Ohm [1e-4,1e-3,1e-2,2,3,4] / Named definition of properties: / Name Value / Drop of voltages, V [du1,du2,du3] / Conductivity, 1/Ohm [k1,k2,k3] / Notes: / Unit properties shall be of the same dimension. / Named properties are set up as local variable of model (or submodel) in Parameters tab or as global signals of the project via Graphics → Signals main menu option.