General Information on SDB Signals data base
[page under construction] / Besides application of signals of the project and programming language global variables (“Parameters” tab of any diagram window) the SimInTech environment allows an external (relative to the project file) data base (DB) to be linked. Data base is linked as an extension module (plug-in) as a dynamic-link library (dll). The standard delivery set of SimInTech includes SDB signals DB (extension module sdb.dll), which can be linked to a project file in “Settings” tab in the project Simulation properties: / With such setting of an extension module of the project data base and data base file name, “Tools” → «Data base editor...”. This item of the main menu becomes accessible. This item activates a dialog box – interface to the data base, in which DB signals can be viewed, populated and edited: / SDB signals data base is a structured data base containing three levels: Categories, Groups of signals and Signals for groups. / Category of signals is a prototype, template or, in terms of programming, a class for data base objects. / Group of signals is a logical unit of the data base and always represents an object of a category. / Signal is a unit physically existing in the memory area: one of variables of the group, which is named and typified. / Thus, the categories create the DB architecture, groups of signals – its population, signals constitute a list of data base signals, which is generated and can be applied in the project. / Signals of a certain group need not necessarily correspond strictly to a template written in the category but this correspondence should desirably be observed except for special validated situations. / The categories ideologically are used for creation of new typical objects of modeling or typical logical (functional) parts of algorithms. Examples of typical objects are: Gate control unit (GCU), Valve control unit (VCU), Motor control unit (MCU), regulator (R27), model of transmitter (Transmitter), etc. Examples of typical functional parts of algorithms are: Preventive protection (PP), Emergency protection (EP), Generation of set points according to sensor readings (Set points), Overlaps, Alarms, Failures, etc. / As a rule, all objects belonging to the same category (of the same type) have similar (the same, in ideal case) sets of properties and parameters, and require the same procedure for processing such parameters at each step of calculation. Thus, such objects can be subject to formalization and formalized and signal vector processing, signal processing as per a template algorithm. Application of standard sub-programs and activation of such sub-programs in typical manner via the interface unit represents another option for processing a group of signals belonging to the same category. The both options can be implemented in SimInTech. / SDB signals DB interface contains: / “Filters” panel, in which user filters influencing on displayed categories, groups of signals and signals of groups can be created and set. The filters does not influence the DB content. Stored filters, when activated, use local filters, which can be manually operated. Use of service character * (asterisk) is allowed in the filters. The filters are stored in a separate file with *.filters extension in the data base file location catalog. / “Categories” panel, in which data base categories can be created and set. / “Groups of signals” panel, in which groups of signals for a selected DB category can be listwisely created, added and deleted. / “Signals and data for groups” panel, in which signals, their default values (initial values) can be created, added, edited and deleted, data types for signals, description and calculation method can be set. It is allowable to select several groups of signals and view signals belonging to several groups listwisely (“Summary table” mode). / Data base save, load and addition keys. / Settings panel for DB settings to be saved in the project.