SimInTech Advantages
SimInTech has the following advantages: / openness – due to implementation of several mechanisms for data exchange with external calculation programs in SimInTech as well as due to built-in programming language and interpreter of mathematical functions; / principle of nesting of structures (nesting depth is not limited), which is especially important for modeling complex dynamical systems or sets of algorithms for a sophisticated engineering object; / vectorization of data transmission and processing algorithms due to implementation of communication lines of data “bus” type and vectorization of inputs/outputs of all typical units; / availability of most complete General engineering and a number of refillable Dedicated libraries of typical units including libraries of thermophysical properties of main working bodies; / availability of graphic primitives and graphics editor with parametrization and script generation enabled, which allows instrumentation panels (boards) to be generated in SimInTech for display and operational control of a system being modeled in the process of calculation; / 16 integration algorithms, including 10 new effective algorithms (5 explicit and 5 implicit ones) for rigid systems of differential equations; / functioning in any version of Windows operating system (XP, Vista, 7, 8, in both 32-bit and 64-bit ones), detailed contextual reference system proved in branch projects and in the process of training.