Global parameters editor window
Global parameters editor window consists of an editor field and a message box (see figure 1): / Figure 1 – Global parameters editor window / Editor field / Values applicable for calculation of each table from an available set of tables can be set in the editor field. Values are entered and calculated according to the rules of built-in SimInTech 4 software system programming language. Figure 2 demonstrates an example for setting ideal gas parameters and calculation of its temperature that then can be used for filling each table to be created. / When working with the global parameters editor window, one can use a tool bar arranged above it: . Commands applicable for working with the global parameters editor window are as follows: Calculate table, View variables, Construct relation, Stepwise debugging and Stop debugging. / Figure 2 – Example for setting constants, arrays and functions in global parameters editor / Show variables command serves for viewing values preset and to be calculated, and is intended to check calculations for correctness. After activation of this command, a window will appear, in which all variables (values) are reduced to one list and have its own value preset or calculated (see figure 3). / Figure 3 – View of variable values / Show relation command allows a vector or scalar relation to be constructed as a scalar function. To construct vector relation Show relation command shall be activated and names of abscissa arrays and names of ordinate arrays shall be indicated in the window opened (see figure 4). / Figure 4 – Relation construction dialog box / As a result the program will construct a relation appearing as a curve (see figure 5): / Figure 5 – Constructed X-Y relation / To construct a scalar relation it shall be indicated in the relation construction dialog box, see figure 6. / Figure 6 – Scalar relation construction dialog box / The following shall be indicated one after another as parameters to construct a relation: minimum limit of construction – min_x, maximum limit of construction – max_x, number of intermediate points between the maximum and minimum limits for constructing a function – count. Function for construction is indicated as an argument to be applied x. / Note that no matter how the description of scalar function appears: function Plus (arg_n), function Minus(argum_1), – x: Plus(x), Minus(x) shall be indicated as a function argument in row Function of Х of Relation construction dialog box. / Constructed scalar relation can be found in figure 7. / Figure 7 – Constructed scalar relation / Stepwise debugging command allows variables to be calculated successively operation by operation. At the same time, the variables window is displayed, which allows the calculation process to be monitored at each step. A current operation (string) of stepwise calculation is highlighted blue in the global variable editor window (see figure 8). / Figure 8 – Example of 1 step in the process of stepwise debugging / Debugging stop command allows stepwise debugging to be stopped. / To calculate all variables and re-plot curves Calculate table command can be applied. / Message window / Message window is intended to display program messages of possible errors or warning messages. In case of an error a relevant message is displayed in the window, while the error string in the editor field is highlighted red. If there are several error messages then double-click the left mouse button on a desired message to select the string corresponding to a required error (see figure 9). / Figure 9 – Example of an error in set parameters