	Step
in palette	| vectorized |

in diagram
The unit generates the output value calculated as per the algorithm: / y(t) = left lbrace stack{ alignl y_1, ~ "if" ~ t > t_0 , # alignl y_0, ~ "if" ~ t <= t_0 , } right none / where t_0 is for response time, y_0 is for initial value, y_1 is for final value , t is for current simulation time given in seconds. / Properties: / Time of activation – t_0 . / Initial state – y_0 . / Final state – y_1 . / The properties can be vectors vec {t_0}= left [ t_{0,1} , t_{0,2} , ... t_{0,n} right ] , vec {y_0}=left [ y_{0,1} , y_{0,2} , ... y_{0,n} right] and vec {y_1}=left [ y_{1,1} , y_{1,2} , ... y_{1,n} right ] , the dimensions of which shall have the same value; in this case the vector will be at the output: / y_i(t) = left lbrace stack{ alignl y_{1,i}, ~ "if" ~ t > t_{0,i} , # alignl y_{0,i}, ~ "if" ~ t <= t_{0,i} . } right none / Examples of filling in the dialog window for unit properties: / Numerical definition of properties: / Name Value / Response time [2] / Initial state [0] / Final state [1] / Named definition of properties: / Name Value / Response time [time_start] / Initial state [y_off] / Final state [y_on] / Mixed definition of properties: / Name Value / Response time [5] / Initial state [y_off] / Final state [y_on] / Vector definition of properties: / Name Value / Response time [3,2] / Initial state [0.0,0.0] / Final state [5.5,6.5] / Notes: / By default the unit generates a scalar output signal. / Named properties are set up as local variables of model (or submodel) in Parameters tab or as global signals of the project via Graphics → Signals main menu option.