	Parabola
in palette	| vectorized |

in diagram
The unit generates the output value calculated as per the formula: / y(t) = a_0 + a_1 cdot t + a_2 cdot t^2 , / where a_0,~a_1,~a_2 are for coefficients, y(t) is for output signal, scalar or vector, t is for current simulation time given in seconds. / Properties: / Free term – coefficient a_0 . / Coefficient at t – coefficient a_1 . / Coefficient at t^2 – coefficient a_2 . / The properties can be vectors vec {a_0}=left [ a_{0,1} , a_{0,2} , ... a_{0,n} right ] , vec {a_1}=left [ a_{1,1} , a_{1,2} , ... a_{1,n} right ] and, the vec {a_2}=left [ a_{2,1} , a_{2,2} , ... a_{2,n} right ] dimensions of which shall be the same; in this case the vector will also be at the output: / vec{y}(t) = vec{a}_0 + vec{a}_1 cdot t + vec{a}_2 cdot t^2 , ~ "or" newline y_i(t) = a_{0,i} + a_{1,i} cdot t + a_{2,i} cdot t^2 , ~ i=1...n. / Examples of filling in the dialog window for unit properties: / Numerical definition of properties: / Name Value / Free term [2] / Coefficient at t [5] / Coefficient at t^2 [1] / Named definition of properties: / Name Value / Free term [a_0] / Coefficient at t [a_1] / Coefficient at t^2 [a_2] / Mixed definition of properties: / Name Value / Free term [5] / Coefficient at t [a_1] / Coefficient at t^2 [1] / Vector definition of properties: / Name Value / Free term [3,1.01] / Coefficient at t [2.1,0.8] / Coefficient at t^2 [1.0,1.2] / Notes: / By default the unit generates a scalar output signal. / Named properties are set up as local variables of model (or submodel) in Parameters tab or as global signals of the project via Graphics → Signals main menu option.