	Polynomial of n-power
in palette	| vectorized |

in diagram
The unit is vectorized and generates the output value calculated as per the formula: / y(t) = a_{0} + a_{1} cdot t + a_{2} cdot t^2 + ... + a_{n} cdot t^{n} , / where a_0 , ~ a_1 , ~a_2 ~...~a_n are for polynomial coefficients, y(t) is for output signal, t is for current simulation time given in seconds. / Properties: / Polynomial coefficients is the vector of coefficients a_0 ,~a_1 ,~a_2 ~...~a_n or several vectors (matrix lines) of coefficients where in the values of polynomial coefficients are defined for a certain output vector element. / If several vectors (matrix lines) is used to define a property then polynomial coefficients are equal to: / A = left [ left [ vec{a}_1 right ],left [vec{a}_2 right ], ... left [ vec{a}_m right ] right ] = left [ [a_{0,1} , a_{1,1} , ... a_{n1,1}], [a_{0,2} , a_{1,2} , ... a_{n2,2}],... [a_{0,m} , a_{1,m} , ... a_{nm,m}] right ] . / In this case a vector signal will be at the output: / y_i(t) = a_{0,i} + a_{1,i} cdot t + a_{2,i} cdot t^2 + ... + a_{n i,i} cdot t^{n i} , ~ i=1...m , / where i is for the number of matrix line of coefficients and the number of output vector element, n i is for the dimension of i-th vector of coefficients (i-th line of the matrix). Dimensions of the vectors can be either the same or different. / Examples of filling in the dialog window for unit properties: / Numerical definition of properties: / Name Value / Polynomial coefficient [2,1,1,5] / Named definition of properties: / Name Value / Polynomial coefficients [c1,c2,c3,c4] / Mixed definition of properties: / Name Value / Polynomial coefficients [k0,k1,0.0,5.7] / Vector definition of properties (matrix consisting of two lines with different dimensions): / Name Value / Polynomial coefficients [[k0,k1,0.0,5.7],[k0,k1,0.0,5.8,0.01]] / Notes: / By default the unit generates a scalar output signal. / Named properties are set up as local variables of model (or submodel) in Parameters tab or as global signals of the project via Graphics → Signals main menu option.