	Sine Curve
in palette

in diagram
The unit is vectorized and generates a sinusoidal output signal: / y(t) = a cdot s i n ( ω cdot t + %phi) , / where a is for the amplitude, %omega is for the circular frequency, 1/s; %phi is for the phase, rad; / t is for the current simulation time in seconds. / Properties: / Amplitude – coefficient a . / Frequency – coefficient %omega . / Phase – coefficient %phi . / The properties can be vectors, which dimensions shall be equal to each other. In this case there will be a vector at the output.