	Normal noise
in palette	| vectorized |

in diagram
The unit generates a pseudorandom sequence of real numbers, which are normally distributed (as per Gauss). / Properties: / Mathematical expectation – M . / Dispersion – D . / Sampling period – T – period of time in seconds, within which a random signal at the unit output will be renewed. If T=0 then a random signal at the unit output will be renewed after completion of every successive step of integration. / The properties can be vectors: vec {M}= left [ M_{1} , M_{2} , ... M_{n} right ] , vec {D}= left [ D_{1} , D_{2} , ... D_{n} right ] and , the vec {T}= left [ T_{1} , T_{2} , ... T_{n} right ] dimensions of which shall be the same; in this case a vector signal will be generated at the output. / Examples of filling in the dialog window for unit properties: / Numerical definition of properties: / Name Value / Mathematical expectation [1] / Dispersion [0.2] / Sampling period [0] / Named definition of properties: / Name Value / Mathematical expectation [M1] / Dispersion [D1] / Sampling period [T_q] / Mixed definition of properties: / Name Value / Mathematical expectation [M1] / Dispersion [1] / Sampling period [0] / Vector definition of properties: / Name Value / Mathematical expectation [M1,M2,M3] / Dispersion [0.1,0.1,0.1] / Sampling period [0,0.01,0.02] / Notes: / By default the unit generates a scalar output signal. / Named properties are set up as local variables of model (or submodel) in Parameters tab or as global signals of the project via Graphics → Signals main menu option.