	Steadystate Noise
in palette

in diagram
The unit is vectorized and generates a pseudorandom sequence of real numbers equally distributed over the range from y_min to y_max . / Properties: / Minimum value – is y_min . / Maximum value – is y_max . / Sampling period ( q_t ) – is the time in seconds a random signal at the unit output will be renewed within. If the sampling period q_t is set to 0 (zero) then a random signal at the unit output will be renewed after execution of any regular step of integration. / The properties can be vectors, which dimensions shall be equal to each other; in this case a vector signal will be generated at the unit output.