	Inverse sawtooth
in palette	|vectorized |

in diagram
The unit generates a periodic linearly decreasing sawtooth signal at the output: / y(t) = left [ 1 - frac left ( {t over T} right ) right ] cdot y_A + y_0 , / where y_A,~T,~y_0 are for unit properties, y(t) is for output signal, t is for current simulation time given in seconds, frac(t/T) is for fractional part. / Properties: / Swing – y_A (height of the “tooth”, signal amplitude). / Period – triangular pulses repetition period T / Offset – y_0 , y-coordinate of the “tooth” (the sawtooth curve lowest point) base. / The properties can be vectors: vec {y_A}= left [ y_{A,1} , y_{A,2} , ... y_{A,n} right ] , vec {T}= left [ T_{1} , T_{2} , ... T_{n} right ] and , the vec {y_0}= left [ y_{0,1} , y_{0,2} , ... y_{0,n} right ] dimensions of which shall be the same; in this case a vector signal will be generated at the output: / y_i(t) = left [ 1 - frac left ( t over T_i right ) right ] cdot y_{A,i} + y_{0,i} , ~i=1...n. / Examples of filling in the dialog window for unit properties: / Numerical definition of properties: / Name Value / Swing [5] / Period [3] / Offset [0] / Named definition of properties: / Name Value / Swing [amp] / Period [T] / Offset [ys] / Mixed definition of properties: / Name Value / Swing [amp] / Period [5] / Offset [0.01] / Vector definition of properties: / Name Value / Swing [amp1,amp2] / Period [1,2] / Offset [0,1] / Notes: / By default the unit generates a scalar output signal. / Named properties are set up as local variables of model (or submodel) in Parameters tab or as global signals of the project via Graphics → Signals main menu option. / The unit is identical to the following design diagram (the Inverse sawtooth properties are defined as equal to 2, 3 and 5): / At the same time (within the first 15 seconds) the output signal diagram is as follows: / Inverse sawtooth