	Triangle signal
in palette	| vectorized |

in diagram
The unit generates a repetitive triangle signal (a half of a signal is Sawtooth and the other half is Inverse sawtooth) at the output: / y(t) = left lbrace stack{ alignl y_A cdot frac left ( {t over T} right ) + y_0 ,~"with"~frac(t/T)<= 0.5 , # alignl y_A cdot left [ 1-frac left ( {t over T} right ) right ] + y_0 , ~"with " frac(t/T)> 0.5 } right none , / where y_A,~T,~y_0 are for unit properties, y(t) is for output signal ,t is for current simulation time given in seconds, frac(t/T) is for fractional part. / Properties: / Swing – y_A (height of the complete “tooth”, signal amplitude). Triangle signal amplitude at the unit output is y_A / 2 . / Period – triangular pulse repetition period T . / Offset – y_0 , y-coordinate of the “tooth” (the sawtooth curve lowest point) base. / The properties can be vectors: vec {y_A}= left [ y_{A,1} , y_{A,2} , ... y_{A,n} right ] , vec {T}= left [ T_{1} , T_{2} , ... T_{n} right ] and , the vec {y_0}= left [ y_{0,1} , y_{0,2} , ... y_{0,n} right ] dimensions of which shall be the same; in this case a vector signal will be generated at the output: / y_i(t) = left lbrace stack{ alignl y_{A,i} cdot frac left ( {t over T_i} right ) + y_{0,i} ,"with "frac(t/T_i)<= 0.5 , # alignl y_{A,i} cdot left [ 1-frac left ( {t over T_i} right ) right ] + y_{0,i} , "with "frac(t/T_i)> 0.5 } right none / Examples of filling in the dialog window for unit properties: / Numerical definition of properties: / Name Value / Swing [5] / Period [3] / Offset [0] / Named definition of properties: / Name Value / Swing [amp] / Period [T] / Offset [ys] / Mixed definition of properties: / Name Value / Swing [amp] / Period [5] / Offset [0.01] / Vector definition of properties: / Name Value / Swing [amp1,amp2] / Period [1,2] / Offset [0,1] / Notes: / By default the unit generates a scalar output signal. / Named properties are set up as local variables of model (or submodel) in Parameters tab or as global signals of the project via Graphics → Signals main menu option. / The comparison of Sawtooth, Inverse Sawtooth and Triangle Signal units: / Sawtooth, Inverse Sawtooth and Triangle Signal: