	From table
in palette	| vectorized |

in diagram
The unit returns values of tabulated argument-dependent functions calculated by the method of linear interpolations at its output. The table is defined as a text file wherein the format of each line shall be as follows: / <argument> <value of function 1> …. <of function N> / Example: / 0.1 1 2 6 9 / 0.2 6 3 7 10 / 0.3 3 5 3 9 / The file is read out one time during initialization of the unit, then it will be interpolated on the basis of loaded data. / Properties: / Number of functions in the file – number of columns with values of functions in the text file. / Data file name – relative path to the table file. / Argument multiplication coefficient – coefficient the simulation time is multiplied by in the course of interpolation.