	General transfer function
in palette	| vectorized |

in diagram
The unit implements the mathematical representation for a circuit, the dynamics of which (for every scalar signal) can be described through the ordinary differential equation (ODE) appearing as follows: / L(p) y(t) ~=~ N(p) cdot u(t) , / where / L(p) cdot y(t) ~=~ a_{n} cdot {{d^{n}y(t)} over {dt^{n}}} ~+~ a_{n-1} cdot {{d^{n-1}y(t)} over {dt^{n-1}}} ~+~ ~...~ + a_{1} cdot {{dy(t)} over {dt}} ~+~ a_0 cdot y(t); newline N(p) cdot u(t) ~=~ b_{m} cdot {{d^{m}u(t)} over {dt^{m}}} ~+~ b_{m-1} cdot {{d^{m-1}u(t)} over {dt^{m-1}}} ~+~ ~...~ + b_{1} cdot {{du(t)} over {dt}} ~+~ b_0 cdot u(t); / a_i,~b_j are for coefficients ( i=0...n,~j=0...m,~n>=m ); / u(t) is for unit input signal (can be vector one, then both the vectors of coefficients and the unit output will be vector ones featuring the same dimension), y(t) is for unit output signal. / With zero initial conditions assumed, the dynamics of the unit can be represented through the following transfer function: / W(s) ~=~ {b_m cdot s^m +...+ b_2 cdot s^2 + b_1 cdot s + b_0} over {a_n cdot s^n +...+ a_2 cdot s^2 + a_1 cdot s + a_0} . / Dimensions of input and output signals, and vectors of coefficients shall be the same. / Properties: / Numerator coefficients – vector b_j with dimension [m]. / Denominator coefficients – vector a_i with dimension [n]. / Initial conditions – vector of initial values y_i(0) of the unit output. / Note: By default the unit implements the processing of a scalar input signal.