	Oscillation element
In palette

In diagram
The unit is vectorized and implements a mathematical model of the element, which dynamics can be described via a linear ordinary differential equation (ODE) as follows: / T_i^2 cdot {{d^2 y_i(t)} over {dt^2}}+2 cdot %beta_i cdot T_i cdot {{dy_i(t)} over {dt}} + y_i(t) ~=~ k_i cdot x_i(t) , / where x_i(t) is for the i-th element of input signal to the unit, T_i is for an element of constant time vector, %beta_i is an element of the damping factors vector, k_i is an element of the amplification factors vector, y_i(t) is for an element of the unit output signal. / In case of zero initial conditions the dynamics of the unit can be represented via the following transfer function: / W \( s \) =k over {T^2 cdot s^2 + 2 cdot T cdot β cdot s + 1} , / that is why the pictogram of the unit has a view of the transfer function of typical oscillation element. / Mandatory condition: T_i <> 0 . / Properties: / The amplification factors – are the vector of factors k_i the input value is multiplied by. / Time constants – are the vector of time constants T_i in seconds. / Damping factor – is the vector of coefficients %beta_i . / The initial conditions – are the vector of initial values y_i(0) for unit output value. / The initial conditions on the derivate –are the vector of initial conditions for the unit output value derivate y_i'(0) . / Note: by default the unit properties are set for the scalar input signal.